# EPHIN/COSTEP

# Level-2 Data Format Specification

for SOHO Archive

Prepared by :			Reinhold Müller-Mellin

Holger Boll

Carsten Scharmberg

April 2000

# Contact address :			Institut für Experimentelle und Angewandte Physik

Olshausenstr. 40, D-24118 Kiel, Germany

Reinhold Müller-Mellin

Phone: (49-431) 880 3227    Fax: (49-431) 85660

e-mail:   mueller-mellin@kernphysik.uni-kiel.de

Holger Boll

Phone: (49-431) 880 4729    Fax: (49-431) 85660

e-mail:   boll@kernphysik.uni-kiel.de

Carsten Scharmberg

Phone: (49-431) 880 2516    Fax: (49-431) 85660

e-mail:   scharmberg@kernphysik.uni-kiel.de

1.	Data Product

The EPHIN instrument (Electron Proton Helium INstrument) forms part of the COSTEP experiment (COmprehensive SupraThermal and Energetic Particle Analyser) within the CEPAC collaboration on bord of the SOHO spacecraft (SOlar and Heliospheric Observatory). For a detailed description of the SOHO mission and the COSTEP experiment see Solar Physics, 162, 1995.

The EPHIN instrument produces scientific data at a constant rate of 172 bit/s or 15 megabit per day and housekeeping data at a rate of 0.25 megabit per day (Level Zero data). This data set is processed at the University of Kiel in two steps yielding Level 1 and Level 2 products. The Level 2 data set is organized in files per day, primarily counting rate information (~ 0.36 megabyte per day) and pulse height analysis information (~ 15 megabyte per day) together with their detached header files. Furthermore a correction file (~0.16 megabyte per day) is included which can be used to correct the counting rates for instrumental effects (e.g. gamma ray and neutron produced background, contamination of one particle species by the other) and to separate isotopes. The distribution medium is CD-ROM. Together with the LION/COSTEP data set one CD-ROM is produced per month. AAREADME and CAVEAT text files are included which can be read by WORD (Text only) or other suitable editors.

# Data Files:

| File Contents | Name Convention |
| --- | --- |
| EPHIN counting rates | EPxyydoy.RL2; 1995 - 1999: x=H since 2000: x=I |
| EPHIN pulse height analysis (PHA) | EPxyydoy.PL2; 1995 - 1999: x=H since 2000: x=I |
| EPHIN rate correction | EPxyydoy.KOR; 1995 - 1999: x=H since 2000: x=I |

# Detached Header Files:

| File Contents | Name Convention |
| --- | --- |
| File header for rate data file | EPxyydoy.MR2; 1995 - 1999: x=H since 2000: x=I |
| File header for PHA data file | EPxyydoy.MP2; 1995 - 1999: x=H since 2000: x=I |

- Counting rates are given as intensities in units of counts/cm2 s sr MeV, a subset of counting rates is given as counting results per accumulation interval of 59.953 seconds. The factors which were used to convert counting results into intensities are given in chapter 5.

- Pulse height words are given as energy deposits in units of MeV. The conversion factors which were used to convert ADC value of a pulse height into MeV are given in chapter 6.

- Rate correction data are given as counts, from which the correction factor can be derived.

- Time resolution for all 3 data sets is 1 minute (exact accumulation period is 59.953 seconds).

# 2.	Data Format Description

# 2.1	Counting rates file: EPxyydoy.RL2

| Item | Label: | Data Type | Data Contents | Units |
| --- | --- | --- | --- | --- |
| 1 2 3 | PB5 Year DOY MS | integer integer integer | year day of year milliseconds of day | year 4 digits day 1 ... 366 ms 0 ... 86,400,000 |
| 4 | S/C Epoch | float (double) | ms since year 0 | ms 14 digits |
| 5 6 | Status Word part 1 Status Word part 2 | Integer Integer | bits 0 to 31 bits 32 to 39 see chapter 3 | binary binary |
| 7 8 9 10 11 12 13 14 | E150 E300 E1300 E3000 P4 P8 P25 P41 | float (E-Fmt) float (E-Fmt) float (E-Fmt) float (E-Fmt) float (E-Fmt) float (E-Fmt) float (E-Fmt) float (E-Fmt) | intensity intensity intensity intensity intensity intensity intensity intensity | /cm2 s sr MeV /cm2 s sr MeV /cm2 s sr MeV /cm2 s sr MeV /cm2 s sr MeV /cm2 s sr MeV /cm2 s sr MeV /cm2 s sr MeV |

# Counting rates file: EPxyydoy.RL2 (continued)

| Item | Label | Data Type | Data Contents | Units |
| --- | --- | --- | --- | --- |
| 15 16 17 18 19 | H4 H8 H25 H41 INT | float (E-Fmt) float (E-Fmt) float (E-Fmt) float (E-Fmt) float (E-Fmt) | intensity intensity intensity intensity intensity | /cm2 s sr MeV/n /cm2 s sr MeV/n /cm2 s sr MeV/n /cm2 s sr MeV/n /cm2 s sr |
| 20 21 22 | P4 GM P4 GR P4 S | integer integer integer | particle count particle count particle count | counts counts counts |
| 23 24 25 | P8 GM P8 GR P8 S | integer integer integer | particle count particle count particle count | counts counts counts |
| 26 27 28 | P25 GM P25 GR P25 S | integer integer integer | particle count particle count particle count | counts counts counts |
| 29 30 31 | P41 GM P41 GR P41 S | integer integer integer | particle count particle count particle count | counts counts counts |
| 32 33 34 35 | H4 GM H4 GR H4 S1 H4 S23 | integer integer integer integer | particle count particle count particle count particle count | counts counts counts counts |
| 36 37 38 39 | H8 GM H8 GR H8 S1 H8 S23 | integer integer integer integer | particle count particle count particle count particle count | counts counts counts counts |
| 40 41 42 43 | H25 GM H25 GR H25 S1 H25 S23 | integer integer integer integer | particle count particle count particle count particle count | counts counts counts counts |
| 44 45 46 47 | H41 GM H41 GR H41 S1 H41 S23 | integer integer integer integer | particle count particle count particle count particle count | counts counts counts counts |
| 48 | Status Flag | integer | see chapter 4 | binary |
| 49 50 51 | Spare Spare Spare |  |  |  |

GM =	Particles incident parallel to sensor axis, passing through both center segments: A0 and B0

(0( ... 21()

GR  =	Particles incident parallel to sensor axis, passing through corresponding ring segments: A1 and B1 or ... or A5 and B5 (0( ... 28()

S1   = 	Particles incident at oblique angle through one center segment and one ring segment: A0 and

B1 or ... or A5 and B0 (0( ... 34()

S23  =	Particles incident at oblique angle through ring segments: A1 and B2 ... or A1 and B3

(0( ... 42()

# 2.2	PHA file: EPxyydoy.PL2

| Item | Label | Data Type | Data Contents | Units/Values |
| --- | --- | --- | --- | --- |
| 1 | S/C Epoch | float (double) | ms since year 0 | ms 14 digits |
| 2 | Co | integer | coincidence type | 0 ... 12 |
| 3 4 5 | Aseg Bseg Pri | integer integer integer | segment det. A segment det. B priority flag | 0 ... 5 0 ... 5 0 or 1 |
| 6 | PHA_A | float (F-Fmt) | energy loss in det. A | MeV |
| 7 | PHA_B | float (F-Fmt) | energy loss in det. B | MeV |
| 8 | PHA_C | float (F-Fmt) | energy loss in det. C | MeV |
| 9 | PHA_D | float (F-Fmt) | energy loss in det. D | MeV |
| 10 | PHA_E | float (F-Fmt) | energy loss in det. E | MeV |
| 11 | E_tot | float (F-Fmt) | total energy loss | MeV |
| 12 13 14 15 | spare spare spare spare |  |  |  |

| Coincid. type | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Channel | E150 | E300 | E1300 | E3000 | P4 | P8 | P25 | P41 | H4 | H8 | H25 | H41 | INT |

2.3	Rate correction file: EPxyydoy.KOR

| Item | Data contents | Data type | Units |
| --- | --- | --- | --- |
| 1 2 3 | year day of year ms of day | integer integer integer | year: 4 digits day: 1...366 ms: 0...86,400,000 |
| 4 | ms since year 0 | float (double) | ms: 14 digits |
| 5 6 7 8 9 | P4 Ptota total # of particles in P4 PHA, arbitrary incidence p+d # particles in proton & deuterium box, arb. incidence Ptotp total # of particles in P4 PHA, parallel incidence p # of particles in proton box, parallel incidence d # of particles in deuterim box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |
| 10 11 12 13 14 | P8 Ptota total # of particles in P8 PHA, arbitrary incidence p+d # particles in proton & deuterium box, arb. incidence Ptotp total # of particles in P8 PHA, parallel incidence p # of particles in proton box, parallel incidence d # of particles in deuterim box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |
| 15 16 17 18 19 | P25 Ptota total # of particles in P25 PHA, arbitrary incidence p+d # particles in proton & deuterium box, arb. incidence Ptotp total # of particles in P25 PHA, parallel incidence p # of particles in proton box, parallel incidence d # of particles in deuterim box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |
| 20 21 22 23 24 | P41 Ptota total # of particles in P41 PHA, arbitrary incidence p+d # particles in proton & deuterium box, arb. incidence Ptotp total # of particles in P41 PHA, parallel incidence p # of particles in proton box, parallel incidence d # of particles in deuterim box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |
| 25 26 27 28 29 | H4 Ptota total # of particles in H4 PHA, arbitrary incidence 3He + 4He # particles in 3He + 4He box, arb.incidence Ptotp total # of particles in H4 PHA, parallel incidence 3He # of particles in 3He box, parallel incidence 4He # of particles in 4He box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |
| 30 31 32 33 34 | H8 Ptota total # of particles in H8 PHA, arbitrary incidence 3He + 4He # particles in 3He + 4He box, arb.incidence Ptotp total # of particles in H8 PHA, parallel incidence 3He # of particles in 3He box, parallel incidence 4He # of particles in 4He box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |
| 35 36 37 38 39 | H25 Ptota total # of particles in H25 PHA, arbitrary incidence 3He + 4He # particles in 3He + 4He box, arb.incidence Ptotp total # of particles in H25 PHA, parallel incidence 3He # of particles in 3He box, parallel incidence 4He # of particles in 4He box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |
| 40 41 42 43 44 | H41 Ptota total # of particles in H41 PHA, arbitrary incidence 3He + 4He # particles in 3He + 4He box, arb.incidence Ptotp total # of particles in H41 PHA, parallel incidence 3He # of particles in 3He box, parallel incidence 4He # of particles in 4He box, parallel incidence | integer integer integer integer integer | counts counts counts counts counts |

Energetic particles can undergo several processes in the EPHIN telescope, which lead to inaccurate particle classification: e.g. electrons can be scattered by large angles, reducing their penetration depth in the detector stack and thus mimicking nuclei, nuclei can pass through insensitive matter like detector mounts, depositing less observable energy, or suffer from nuclear interaction in the silicon detector. This is to a large degree unavoidable, but can be corrected to some degree by pulse height analysis. Using ground data from accelerator calibration and flight data from the first 8 months of SOHO operation, calibration curves for the various nuclei species were established. Boxes around these curves allow elemental and isotopic separation for protons, deuterium, helium-3 and helium-4. Restriction to only particles incident parallel to the optical axis of the telescope decreases the path length variation, thereby increasing the isotopic resolution at the expense of statistical accuracy. To improve on statistics, averaging over longer time periods may be carried out. Owing to multiple scattering there is no easy correction available for electron channels.

How to correct the counting rates:

1. divide the number of PHA counts in the box by the total number of PHA counts

2. apply this correction factor to the associated counting rate

Example for arbitrary incidence:

item 6 of EPxyydoy.KOR

P4 corrected   =   P4 uncorrected ( = item 11 of EPxyydoy.RL2) • ((((((((((((

item 5 of EPxyydoy.KOR

Example for parallel incidence:

item 20 + item 21 of EPxyydoy.RL2         item 8 + item 9 of EPxyydoy.KOR

P4 corrected  =  ((((((((((((((((   •   ((((((((((((((((

59.953  •  1.02  •  3.5                             item 7 of EPxyydoy.KOR

Note: for parallel incidence the counting results must be converted into intensities. The geometric factor for the sum of six segments (P4GM+P4GR) is about 5 % less than 6 times the geometric factor for the center segments (Ring A/B OFF, see chapter 5).

How to average corrected fluxes over n minutes:

1     n

Average   =   (    (     ( counting rate • correction factor )

n   i = 1

# 2.4	Header for Rate Data File: EPxyydoy.MR2

Example:

# University of Kiel, Extraterrestrial Physics Group

# PI: Horst Kunow

Program: GENSCIL2, Author: Holger Boll, Jan-97

Program_Version: 1.0

Data_Version: V01

Project: SOHO-COSTEP

Instrument: EPHIN

Data_Type: Rates

Data_File_Name:EPH97001.RL2

Data_File_Type: ASCII

Generation_Date: Tue Feb 18 16:48:43 1997

Data_Period_Start: 1997-01-01 00:01:10

Data_Period_End  : 1997-01-01 23:59:02

Parameter_File_Name: EPH_IFAC.PRO

2.5	Header for PHA Data File: EPxyydoy.MP2

Example:

# University of Kiel, Extraterrestrial Physics Group

PI: Horst Kunow

Program: GENPHAL2, Author: Holger Boll, Jan-97

Program_Version: 1.0

Data_Version: V01

Project: SOHO-COSTEP

Instrument: EPHIN

Data_Type: Pulse Height Analysis

Data_File_Name: EPH97001.PL2

Data_File_Type: ASCII

Generation_Date: Thu Feb 13 14:15:58 1997

Data_Period_Start: 1997-01-01 00:01:10

Data_Period_End  : 1997-01-01 23:59:02

Parame	ter_File_Name: PHA_BIN_ENERG.PRO

3.	EPHIN Status Word

The EPHIN status word in words 5 and 6 of the counting rate file is implemented by hardware in the onboard EPHIN electronics and telemetered to ground. Its unrestricted use requires detailed knowledge of the EPHIN hardware. For data evaluation by scientists less familiar with the hardware, an EPHIN status flag in word 48 of the counting rate file has been implemented by software (see chapter 4).

| Label | Bit | EPHIN Status Information |
| --- | --- | --- |
|  | Position | MSB |  |  |  |  |  |  | LSB | Comment |
| Status part 1 | 31 – 24 | N/U | FMB | FMB5 | FMB4 | FMB3 | FMB2 | FMB1 | FMB0 | Fail. mode |
| default |  | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Det. B |
| Status part 1 | 23 – 16 | Ring | FMA | FMA5 | FMA4 | FMA3 | FMA2 | FMA1 | FMA0 | Fail. mode |
| default |  | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Det. A |
| Status part 1 | 15 – 8 | N/U | Reset | Wdog | PROM | SRAM | RAM | Dwnld | Upld | CPU status |
| default |  | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |  |
| Status part 1 | 7 – 0 | Op Mode | SIO Fr | SIO Ovr | SIO Par | Minute Counter | mode, error, |
| default |  | 0 | 1 | 0 | 0 | 0 | X | X | X | frame count |
| Status part 2 | 31 – 8 | N/U |  |
| default |  | 0 |  |
| Status part 2 | 7 – 0 | Det.G | Det.A-F | An.Pow | FMG | FMF | FME | FMD | FMC | Power and |
| default |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Fail. mode |

# N/U = not used		SIO Fr, Ovr, Par = Serial Input Output framing error, overrun error, parity error

X     = don’t care	Wdog = watchdog event

Op mode 00 = standby, 01 = nominal operation, 10 = calibration, 11 = not allowed

# 4.	EPHIN Status Flag

The EPHIN status flag shall facilitate the use of the EPHIN data set without detailed knowledge of the EPHIN hardware status bits and their effects. The status flag is generated by ground software. It is located in word 48 of the counting rate file. The contents of the status flag is a decimal code which results from the summation of the flag bit values.

| Flag Bit Value | Remarks |
| --- | --- |
| 0 | Nominal observation, i.e. High Voltage ON, no failure mode, ring segment switching disabled |
| 1 | Failure mode E |
| 2 | Ring A/B OFF |
| 4 | E patch uploaded |
| 8 | Commissioning |
| 16 | Standby or maintenance, i.e. High Voltage OFF |
| 32 | Calibration, i.e. test mode |
| 64 | Ring segment switching enabled |
| 128 | TBD |

4.1	Status Flag History

A status flag history is given from first switch-on in December 1995 until February 1998. The status flag is valid from the time indicated until a new status flag is listed. An updated list of the status flag is included on the Level 2 distribution medium (see CAVEAT.TXT).

| Year | Month | Day | Hour | Minute | Status Flag | Change |
| --- | --- | --- | --- | --- | --- | --- |
| 1995 | 12 | 07 | 17 | 28 | 16 | EPHIN ON (standby or maintenance) |
| 1995 | 12 | 07 | 17 | 35 | 0 | Nominal observation |
| 1995 | 12 | 09 | 17 | 03 | 8 | Commissioning |
| 1995 | 12 | 10 | 05 | 15 | 0 | Nominal observation |
| 1996 | 10 | 31 | 14 | 47 | 1 | Failure mode E |
| 1996 | 12 | 12 | 16 | 42 | 3 | Ring A/B OFF (for check-out only) |
| 1996 | 12 | 18 | 14 | 45 | 1 | Ring A/B ON (back to normal) |
| 1997 | 02 | 15 | 10 | 25 | -1 | EPHIN OFF (no data) |
| 1997 | 02 | 16 | 16 | 37 | 16 | EPHIN ON (standby or maintenance) |
| 1997 | 02 | 16 | 16 | 45 | 0 | Nominal observation |
| 1997 | 02 | 19 | 14 | 57 | 1 | Failure mode E |
| 1997 | 03 | 13 | 14 | 41 | 5 | Upload E patch (salvage PHA_E) |
| 1997 | 04 | 23 | 16 | 19 | 37 | Calibration |
| 1997 | 04 | 23 | 16 | 28 | 5 | End calibration |
| 1997 | 08 | 22 | 13 | 10 | 5 | Upload histogram patch (parallel incidence) |
| 1997 | 10 | 10 | 14 | 39 | 69 | Enable ring segment switching |

Note:

- The code -1 (no data) is dummy. It will not show up in L2 data records as it is only introduced for the purpose of machine reading above table.

- The first table or software upload after EPHIN ON will set bit 22 (value 4). It can only be cleared by power cycling or by a reset command. A second upload will not be recognizable as a status change (see e.g. histogram patch on 22-AUG-97).

4.2	Example

In order to select data which are taken with EPHIN in observation mode (not always nominal !) the flag shall have the following contents:

| Start | Stop | Status Flag | Remarks |
| --- | --- | --- | --- |
| 07-DEC-95 | 09-DEC-95 | 0 | Nominal observation |
| 10-DEC-95 | 31-OCT-96 | 0 | Nominal observation |
| 31-OCT-96 | 12-DEC-96 | 1 | Failure mode E Rates: E3000, P41, H41 show zero counts, corresponding events are counted together with E1300, P25, H25, hence use larger energy window. PHA: no PHA words for E3000, P41, H41, corresponding events are pulse height analyzed as E1300, P25, H25, pulse heights for E (PHA_E) are lost. |
| 12-DEC-96 | 18-DEC-96 | 3 | Failure mode E with ring A/B OFF Rates: as in failure mode E above but use small geometry factor PHA: as in failure mode E above |
| 18-DEC-96 | 19-FEB-97 | 1 | Failure mode E (see above) |
| 19-FEB-97 | 10-OCT-97 | 5 | Failure mode E with upload of E-patch, i.e. recovery of PHA_E Rates: as in failure mode E above PHA: no PHA words for E1300, P25, H25 events corresponding events are pulse height analyzed as E3000, P41, H41. PHA_E = zero for true E1300, P25, H25 events PHA_E > zero for true E3000, P41, H41 events. |
| 10-OCT-97 | > FEB-98 | 69 | Failure mode E with upload of E-patch and automatic ring segment switching enabled Irregular status changes may occur automatically: "RING A/B OFF", i.e. bit value 2 is added (flag =71). This status change is event driven, it switches to the low geometric factor during high fluxes. On detection of low fluxes, the ring segments are switched back on again. The occurrence is not recorded in this table. |

5.	EPHIN Intensity Factors

Part of the Level-2 counting rates are already converted into intensities [counts/(cm2 s sr MeV/n)] by dividing the counting rates [counts/s] through the intensity factor:

Intensity Factor   =   Geometry Factor   (   Energy Window   [cm2 sr MeV/n]

The factors vary with observation modes of EPHIN. The following observation modes with influence on the intensity factor have been in use during the SOHO prime mission:

| Observation Mode | Description |
| --- | --- |
| nominal mode | High voltage on, all detectors logically on |
| failure mode E | High voltage on, detector E logically off |
| ring A/B off | High voltage on, segments A1 … A5 and B1 … B5 logically off and respective preamplifier power off |

Geometry Factor:		units:	cm2 sr

| Geometry factor: nominal observation mode |
| --- |
| 0.25 | 1.78 | 2.01 | 1.58 | E150, E300, E1300, E3000 |
| 5.14 | 5.14 | 4.77 | 3.8 | P4, P8, P25, P41 |
| 5.14 | 5.14 | 4.77 | 3.8 | H4, H8, H25, H41 |
| 6.85 |  |  |  | INT |

| Geometry factor: failure mode E |
| --- |
| 0.25 | 1.78 | 1.8 | 1. | E150, E300, E1300, E3000 |
| 5.14 | 5.14 | 4.29 | 1. | P4, P8, P25, P41 |
| 5.14 | 5.14 | 4.29 | 1. | H4, H8, H25, H41 |
| 7.84 |  |  |  | INT |

| Geometry factor: ring A/B off and failure mode E |
| --- |
| 0.01 | 0.14 | 0.11 | 1. | E150, E300, E1300, E3000 |
| 0.18 | 0.18 | 0.18 | 1. | P4, P8, P25, P41 |
| 0.18 | 0.18 | 0.18 | 1. | H4, H8, H25, H41 |
| 0.36 |  |  |  | INT |

Note: The combination ring A/B off without failure mode E will probably never occur.

Energy Window:		units:	MeV or MeV/n

| Energy window: nominal observation mode |
| --- |
| 0.45 | 2.3 | 3.6 | 5.2 | E150, E300, E1300, E3000 |
| 3.5 | 17.2 | 16. | 12. | P4, P8, P25, P41 |
| 3.5 | 17.2 | 16. | 12. | H4, H8, H25, H41 |
| 1. |  |  |  | INT |

| Energy window: failure mode E |
| --- |
| 0.45 | 2.3 | 7.4 | 1. | E150, E300, E1300, E3000 |
| 3.5 | 17.2 | 28. | 1. | P4, P8, P25, P41 |
| 3.5 | 17.2 | 28. | 1. | H4, H8, H25, H41 |
| 1. |  |  |  | INT |

Note:

- No energy window is given for the integral counter INT. The geometry factor given is twice the forward incident factor assuming an idealized response for forward and backward incident particles. The actual factor is somewhat lower due to absorption in the spacecraft matter.

- Switching ring segments off does not change the energy window

6.	EPHIN PHA conversion factors

The Level 2 data in the PHA files are given in units of MeV. The following conversion factors were used to convert the telemetered channel number TLMi, i.e. the analog-to-digital converter result of a pulse height, into energy deposit PHAi in MeV for detector i:

TLMi

PHAi  =   (((  (  Factori

1023

where Factori can be either the low range factor or high range factor, depending on the Low/High flag of the telemetered pulse height word.

| Detector pulse height | Low range factor | High range factor |
| --- | --- | --- |
| PHA_A | 3.00 | 30.00 |
| PHA_B | 3.00 | 45.00 |
| PHA_C | 16.07 | 166.7 |
| PHA_D | 20.00 | 225.00 |
| PHA_E | 20.00 | 225.00 |